## Slide 1
HOME AUTOMATION · 2026
The State of the Smart Home
Where we've been, where we are, and where we're going.
Jim Johnson
35+ years in home automation · SMMUG · May 11, 2026
Notes: Welcome and thank SMMUG for having you. This is a survey talk - 35 years of context distilled into one evening. Audience promise: by the end you'll know who the players are, what the standards mean, why Apple's approach is different, and what to actually buy. Tone reminder: dial down jargon. If you say a protocol name, give a one-line plain-English translation.

## Slide 2
ABOUT YOUR SPEAKER
Jim Johnson
Three and a half decades in home automation - from X10 modules to Matter.
Long history
Watched the industry evolve from light switches and timers to AI-driven ambient computing.
Hands-on user
HomeSeer → Wink → Homey Pro and Hubitat Elevation C-8 Pro today. Also a Home Assistant tinkerer.
Translator
My job tonight: take the technical and make it useful - not lose you in acronyms.
SMMUG · The State of the Smart Home · May 11, 2026
Introduction
2
Notes: I've been doing this long enough to have stories about products that no longer exist - and that's actually one of the running themes tonight. Quick wave-of-hands: who here has tried to set up a smart bulb? A smart lock? Who's given up on something? Promise: I'll keep this practical. If you only remember three things tonight, I want it to be (1) Matter changes the game, (2) Apple Home is finally credible, (3) local control beats cloud control.

## Slide 3
TONIGHT'S ROADMAP
What we'll cover
01
A brief history
From X10 to Matter - 50 years in 5 minutes
02
Industry consolidation
Who bought whom, and who's left standing
03
Standards & protocols
Wi-Fi, Zigbee, Z-Wave, Thread, Matter, BLE
04
Apple's smart-home story
Late to the party, but the party is at their house now
05
Hubs - local vs cloud
Why the brain of your home matters
06
Voice + AI
Alexa+, Gemini, Siri, and what's coming
07
Privacy, security & graveyards
The data, the breaches, and the stranded users
08
Where we're going
Predictions and recommendations
SMMUG · The State of the Smart Home · May 11, 2026
Agenda
3
Notes: Quick roadmap so people know what's coming and don't have to interrupt. Tell them: 'Save questions until each section break - or shout them, this is a small room.' If we run long, sections 7-8 are the most cuttable. Sections 3 and 4 are the heart.

## Slide 4
PART ONE
A Brief History
From a Scottish company called Pico Electronics to the screens in your pocket.
Notes: Section break - take a breath, sip water. Tease X10: 'The first commercial home automation system was invented in 1975 in Glenrothes, Scotland - to control lamps with carrier signals over power lines.'

## Slide 5
PART 1 · ORIGINS
It started with a power line
X10 - 1975
Invented by Pico Electronics in Glenrothes, Scotland - the first commercially available home automation system.
It used your home's existing AC wiring to send tiny digital pulses on top of the 60 Hz power line.
A controller could address up to 256 devices using 'house codes' (A-P) and 'unit codes' (1-16).
Quirky, slow, and unreliable - but it worked for 40+ years and is still installed in homes today.
50
YEARS AGO
X10 launched the same year as
Microsoft (April 1975)
· two years before the Apple II.
SMMUG · The State of the Smart Home · May 11, 2026
History
5
Notes: Anecdote: show of hands - who in this room ever owned an X10 module? (Often half the room in a Mac group.) X10 worked because it didn't need new wiring - powerline carrier signals. Reliability problems: noise from CFLs, switching power supplies, surge protectors, even some neighbors' devices on the same transformer. Still a great way to anchor the talk - this is the genesis of the whole industry.

## Slide 6
PART 1 · TIMELINE
50 years of home automation, at a glance
1975
X10
Pico Electronics ships powerline carrier modules.
1984
CEBus
Industry consortium tries a standard. (Doesn't catch on.)
1999
Z-Wave
Sub-GHz mesh from Zensys (Denmark).
2002
Zigbee
Mesh networking on 802.15.4.
2011
Nest
Smart thermostat - design changes everything.
2014
HomeKit
Apple finally enters. SmartThings + Wink launch.
2014
Echo / Alexa
Voice in the living room.
2018
Thread
IPv6 mesh born at Nest, opened to all.
2022
Matter 1.0
Apple + Google + Amazon + Samsung agree on something.
2026
AI agents
LLMs move from chat to your house.
Each wave solved a problem the last couldn't - and created a new one.
SMMUG · The State of the Smart Home · May 11, 2026
History
6
Notes: Walk left to right. Don't read every entry - point and narrate. X10 → mesh radios (Z-Wave/Zigbee) solve reliability and battery devices. Nest (2011) is the moment design enters the space - people start buying smart home stuff because it's pretty, not because they're hobbyists. 2014 is the inflection year: HomeKit, SmartThings, Wink, and Echo all in 12 months. Thread 2018 - critical because it's IP-based mesh, so devices talk to the internet without a translator. Matter 2022 - the first time the four big platforms all signed the same dotted line. AI agents 2026 - we're standing in the doorway.

## Slide 7
PART 1 · THE FIRST WAVE
Mesh radios: Z-Wave, Zigbee, Insteon
Why they mattered: battery-powered sensors and door locks that X10 could never support.
Z-Wave
1999 · Zensys (Denmark) → Silicon Labs
Sub-GHz radio (908 MHz in the US). Mesh network. Up to ~232 devices. Slow, but reliable - barely fights with Wi-Fi because it's on a different band entirely.
Zigbee
2002 · IEEE 802.15.4 + Zigbee Alliance
2.4 GHz radio. Open standard, big ecosystem (Hue, IKEA, Aqara, SmartThings). Cheap chips, lots of choice - but it lives on the same band as Wi-Fi and microwave ovens.
Insteon
2005 · SmartLabs (USA)
Powerline + RF dual-band - a clever evolution of X10 with better reliability. Beloved by enthusiasts. Company collapsed twice (2022, 2024), bricking servers and leaving users stranded.
SMMUG · The State of the Smart Home · May 11, 2026
History
7
Notes: Why mesh? Because a sensor on a window ledge needs to run on a coin cell for a year. Wi-Fi will drain a coin cell in a day. Z-Wave's killer feature is interoperability certification - one logo means it actually works with other Z-Wave devices. Zigbee in its early years was famously fragmented (Hue Zigbee, SmartThings Zigbee, Xiaomi Zigbee - all 'Zigbee', none talking to each other) - Matter is supposed to fix that. Insteon story is a cautionary tale we'll come back to in the graveyard section.

## Slide 8
PART 1 · THE SMARTPHONE ERA
Apps changed everything (2010s)
Once everyone had an iPhone, the smart home was no longer a hobby for engineers.
Nest (2011)
A thermostat that learned. Sold to Google for $3.2B in 2014.
Philips Hue (2012)
Smart bulbs over Zigbee. The bulb that taught the world about color temperature.
Amazon Echo (2014)
Voice in the living room. The first device most people called 'AI'.
IFTTT / Stringify
If-this-then-that automation made by users, not coders. (Stringify died in 2018.)
SMMUG · The State of the Smart Home · May 11, 2026
History
8
Notes: Nest is the moment design entered. Tony Fadell (iPod) and Matt Rogers came out of Apple to build it. Hue made smart bulbs mainstream. Also accidentally taught the whole industry the Zigbee Light Link profile. Echo was the surprise hit - Amazon almost killed Alexa internally before launch. IFTTT was beloved by tinkerers, then locked everything behind a $5/mo paywall in 2020. Stringify died entirely. Lesson seeded: cloud services have an expiration date.

## Slide 9
PART TWO
Industry Consolidation
Five companies own most of what's in your home.
Notes: Transition: 'Now that we've got the history, let's talk about who actually owns this stuff today - because it's a much shorter list than you'd think.'

## Slide 10
PART 2 · THE GREAT ACQUISITIONS
Who bought whom
Acquirer | Acquired | Year | Price | What it bought them
Google | Nest | 2014 | $3.2 B | Thermostats, smoke alarms, design pedigree
Amazon | Ring | 2018 | ~$1.0 B | Video doorbells, neighborhood surveillance
Amazon | Blink | 2017 | $90 M | Battery-powered cameras
Amazon | eero | 2019 | $97 M | Mesh Wi-Fi - and a Thread border-router footprint
Samsung | SmartThings | 2014 | $200 M | The DIY hub of its day
Resideo / Honeywell | Snap One (Control4) | 2024 | $1.4 B | Pro-installer market
Assa Abloy | August / Yale | 2017+ | — | Smart locks across multiple brands
Generac | ecobee | 2021 | $770 M | Thermostats, sensors, software
Apple has acquired almost no smart-home companies - their strategy is to set the rules, not to roll up the market.
SMMUG · The State of the Smart Home · May 11, 2026
Consolidation
9
Notes: Headline: in roughly a decade, the independent smart-home brands you fell in love with mostly belong to four companies now. Google + Nest: a slow integration - users felt orphaned for years. Amazon + Ring: controversial because of police partnerships (we'll come back to this in privacy). Resideo/Snap One/Control4: this is the pro-install consolidation, often invisible to consumers but huge in dollars. Apple line is important - they don't acquire, they extend HomeKit/Matter and let others meet their bar.

## Slide 11
PART 2 · THE MAP TODAY
Who actually runs your home
Amazon
Voice + cameras + mesh Wi-Fi
Alexa · Ring · Blink · eero
Google
Voice + thermostats + cameras
Google Home · Nest · Chromecast
Apple
Privacy-first platform
Apple Home · HomePod · Apple TV
Samsung
DIY hub + cross-brand SmartThings
SmartThings · Family Hub
Resideo / Snap One
Pro install dominance
Control4 · Honeywell Home
Crestron / Savant
Luxury & commercial
Crestron Home · Savant Pro
SMMUG · The State of the Smart Home · May 11, 2026
Consolidation
10
Notes: Audience anchor: name the brands and watch heads nod. Note Apple's line - 'privacy-first platform.' Apple doesn't make the most devices; they set the rules for who connects. Crestron/Savant are basically invisible to the consumer market but they own homes that cost more than the SMMUG building. Big point: in a $100B+ industry, six players carry most of the volume - this is the consolidated market.

## Slide 12
PART THREE
Protocols & Standards
Wi-Fi, Bluetooth, Zigbee, Z-Wave, Thread - and the new common language called Matter.
Notes: This is the deepest technical section. Promise the audience: I'll keep this concrete - what each one does, what's good about it, and when you'd pick it. If they remember nothing else: 'Matter is what they talk in. Thread is how they talk.'

## Slide 13
PART 3 · ORIGINS OF MATTER
The consortium that finally agreed
It started as Project CHIP — Connected Home over IP — announced in December 2019 by Amazon, Apple, Google, and the Zigbee Alliance.
The Zigbee Alliance renamed itself the Connectivity Standards Alliance (CSA) in 2021. Matter 1.0 shipped in October 2022.
Apple
Pushed Wi-Fi + Thread, secure commissioning, identity model from HomeKit.
Google
Brought Thread (born at Nest) and Weave codebase for the foundation.
Amazon
Brought scale - the largest installed base of smart speakers and routers.
Samsung + 400 more
Bulb makers, lock makers, chip vendors. Hundreds of companies signed on.
SMMUG · The State of the Smart Home · May 11, 2026
Standards
11
Notes: This is the 'first time the big four agreed on anything' moment. Worth pausing on the absurdity: Apple, Amazon, and Google had built incompatible empires for a decade - and then sat at the same table. Matter is royalty-free, open source on GitHub. That's almost unprecedented for these companies. Worth noting: the spec is 1,000+ pages. The 'simple' part is for consumers - the engineering is enormous.

## Slide 14
PART 3 · MATTER
What Matter actually is
Matter is an application-layer standard.
It says HOW devices describe themselves and HOW commands flow. It doesn't replace your radios - it sits on top of them.
01
Runs over IP
Wi-Fi, Ethernet, and Thread. No more 'is this Zigbee or Z-Wave?' headaches for users.
02
Local first
Devices control each other on your LAN. Cloud is optional, not required.
03
Multi-admin
One bulb can be controlled by Apple Home AND Alexa AND Google Home at the same time.
SMMUG · The State of the Smart Home · May 11, 2026
Standards
12
Notes: Multi-admin is the headline feature. Before Matter, your bulb was locked into one ecosystem. Now you can hand the same physical bulb to Apple AND Google. Local-first is the privacy and reliability story. If your internet dies, your lights still work. Important caveat: Matter is over-promised. We'll talk about the messy reality on the next slide.

## Slide 15
PART 3 · THREAD
Thread - the mesh that speaks IP
Think of Thread as Wi-Fi for tiny, battery-powered things. No router needed - the devices themselves form the network.
Born inside Nest. Released as an open standard in 2014 through the Thread Group.
Runs on 802.15.4 — same physical radio as Zigbee — but with IPv6 baked in.
Self-healing mesh: every powered device acts as a router.
Battery devices sleep most of the time and wake up to talk.
Needs a 'border router' to bridge Thread to your LAN — HomePod mini, Apple TV 4K, Nest Hub, eero 6+, etc.
You probably already own one and didn't know it.
Border routers
you already own
HomePod mini / HomePod (2nd gen)
Apple TV 4K (2nd gen and later)
Nest Hub (2nd gen), Nest Hub Max
eero 6, 6+, 6 Pro, Pro 7
Samsung SmartThings hubs
SMMUG · The State of the Smart Home · May 11, 2026
Standards
13
Notes: Key one-liner: 'Thread is the radio Matter rides on for low-power devices.' Border router analogy: 'Thread is its own little neighborhood. The border router is the post office that takes mail in and out.' Apple TV / HomePod doubling as Thread border routers is a *huge* convenience for this audience - they probably already have one.

## Slide 16
PART 3 · SIDE-BY-SIDE
Protocols at a glance
Protocol | Band | Range | Power use | Strength | Weakness
Wi-Fi | 2.4 / 5 / 6 GHz | 30-50 m | High | Fast, ubiquitous | Battery killer; congestion
Bluetooth LE | 2.4 GHz | 10-30 m | Very low | In every phone | Short range; pairing pain
Zigbee | 2.4 GHz | 10-30 m mesh | Very low | Cheap, huge ecosystem | Same band as Wi-Fi; fragmented
Z-Wave | 908 MHz (US) | 30-100 m mesh | Very low | Reliable, certified | Slower, fewer device options
Thread | 2.4 GHz | 10-30 m mesh | Very low | IP-native, self-healing | Needs a border router
Matter | (over Wi-Fi / Thread) | — | — | Common language across all | Still maturing in 2026
Bottom line: you'll always have at least three radios in the house. Matter just makes them speak the same language.
SMMUG · The State of the Smart Home · May 11, 2026
Standards
14
Notes: Don't read the table verbatim. Anchor on the rightmost two columns: strength and weakness. Wi-Fi: great until you have 60 devices on the same band. Z-Wave: the 'just works' protocol of the last 15 years - lower bandwidth but rock-solid. Thread: the future of low-power. Matter rides on it. Reinforce: the radio doesn't matter to the user anymore - Matter is what makes the 'wait, will this work with my system' question go away (eventually).

## Slide 17
PART 3 · DEEP DIVE
Zigbee — the workhorse
PROS
CONS
Open standard, hundreds of manufacturers
Cheap chips → cheap devices
Battery-efficient mesh
Huge installed base (Hue, IKEA, Aqara, Tuya, SmartThings)
Direct device-to-device routing without internet
Same 2.4 GHz band as Wi-Fi and microwaves
Historically fragmented profiles (HA, ZLL, ZHA)
Pairing rituals can be finicky
Vendor-specific extensions break interoperability
Slowly being eclipsed by Thread + Matter
SMMUG · The State of the Smart Home · May 11, 2026
Standards
15
Notes: Zigbee is what's in most Hue bulbs, most IKEA Tradfri stuff, most Aqara sensors, most Chinese white-label devices. Fragmentation story: until Zigbee 3.0 (2016), buying a 'Zigbee' bulb didn't guarantee it worked with another 'Zigbee' hub. Most Zigbee devices can be re-pinned as Matter over Thread by manufacturers, but it requires new silicon - so we'll have Zigbee around for another decade easily.

## Slide 18
PART 3 · DEEP DIVE
Z-Wave — quiet, reliable, getting open
PROS
CONS
Sub-GHz - doesn't fight Wi-Fi or Bluetooth
Longer range than Zigbee, especially in walls
Strict interoperability certification
Z-Wave Long Range (LR) hits 1+ mile line of sight
Z-Wave 800-series is genuinely faster and lower power
Smaller ecosystem - fewer device options
Was proprietary to Silicon Labs for decades (now opening)
More expensive per device than Zigbee
Mostly North America - global SKUs are a mess of frequencies
Apple Home doesn't speak Z-Wave directly (need a hub)
SMMUG · The State of the Smart Home · May 11, 2026
Standards
16
Notes: If you ask installers what's most reliable, they'll say Z-Wave or Lutron Caseta - because they're both sub-GHz. Z-Wave Alliance opened the spec in 2020. Z-Wave LR is the long-range variant - genuinely impressive on big properties. Apple Home doesn't talk Z-Wave directly, so for Apple users it means: get a hub (Hubitat, Home Assistant, SmartThings) that bridges Z-Wave to Apple Home.

## Slide 19
PART 3 · DEEP DIVE
Wi-Fi + Bluetooth
What your phone already speaks - the convenient default that doesn't scale.
Wi-Fi
Pros
Fast (great for cameras, streaming)
No new hub needed
Familiar to every user
Cons
Power-hungry (battery devices suffer)
Congestion: 50+ devices crushes consumer routers
Single point of failure - router down = house down
Bluetooth LE
Pros
In every phone, watch, tablet
Excellent for proximity (locks, beacons)
Pairs without a hub
Cons
Short range, no real mesh in practice
Pairing UX still frustrating after 25 years
Cloud often required for remote control
SMMUG · The State of the Smart Home · May 11, 2026
Standards
17
Notes: Wi-Fi smart bulbs are seductive (no hub!) but they kill router performance at scale. Quick rule of thumb: under 20 devices, Wi-Fi-only is fine. Over 50, you want Thread or Zigbee or Z-Wave for the small stuff. Bluetooth shines for door locks (proximity) and pairing - and Matter actually uses BLE for the initial pairing handshake.

## Slide 20
PART 3 · REALITY CHECK
Matter in 2026 - what's real, what's not
Working well
Light bulbs, plugs, switches
Thermostats (basic)
Window blinds and shades
Door/window sensors
Multi-admin (controlling one device from multiple ecosystems)
Partial / awkward
Locks (most still need vendor app for advanced features)
Robot vacuums (basic 'run / pause' only)
Cameras (Matter 1.3+, vendor support still patchy)
Bridging from Zigbee / Z-Wave gear
Pairing UX still rough on edge cases
Still missing
Energy management beyond the basics
Doorbells with two-way audio
Major appliances at depth
Garage doors (improving)
Anything truly 'pro install' grade
SMMUG · The State of the Smart Home · May 11, 2026
Standards
18
Notes: Be honest with the audience: Matter is real, but it's not finished. The good news: the boring devices (bulbs, plugs) are genuinely solid in 2026. Locks are the wedge category - they work, but if you want auto-lock-on-departure or guest codes, you still live in the vendor app. Cameras over Matter only landed in Matter 1.3 (mid 2024). Adoption is slow.

## Slide 21
PART FOUR
Apple's Smart-Home Story
Late to the party. Then they redecorated the room.
Notes: This is the most important section for this audience. Spend time here. Acknowledge: 'For years, smart home enthusiasts told us not to use Apple Home. That advice has finally aged out.'

## Slide 22
PART 4 · APPLE'S LATE ENTRY
Apple was late, on purpose
Amazon shipped Echo in November 2014. Google bought Nest in January 2014. Apple announced HomeKit in June 2014 - but with no app and no products until iOS 9 in 2015, and no native Home app until 2016.
Why?
Required a dedicated security chip (MFi) in every accessory
Required end-to-end encryption from device to phone
Refused to centralize user data in their cloud
Refused to launch a hub - your iPad / Apple TV had to be it
“
Apple's bar was so high that most manufacturers had to redesign their hardware just to wear the HomeKit logo.
That's why it took 5+ years to feel mainstream.
SMMUG · The State of the Smart Home · May 11, 2026
Apple
19
Notes: The MFi chip requirement was hated by manufacturers - it added cost and lock-in. Apple eventually relaxed it to a software-only attestation around 2018. But the rigor paid off: HomeKit devices remain among the most secure in the industry. Audience anecdote: if you bought a smart device in 2015 and it didn't have the 'Works with HomeKit' badge, it usually meant the maker couldn't pass Apple's security audit.

## Slide 23
PART 4 · PHILOSOPHY
Three things Apple did differently
End-to-end encryption
Your home data is encrypted with keys only your devices hold. Apple's servers can't read it.
Local-first by design
Automations run on your hub (HomePod, Apple TV) - not in the cloud. Works without internet.
Identity over device
Permissions are tied to your Apple ID and people you share the home with - not gadget pairing.
SMMUG · The State of the Smart Home · May 11, 2026
Apple
20
Notes: Anchor: 'These three choices are why people who care about privacy ended up at Apple Home, even though Amazon and Google had more devices.' Local-first is the most important. Apple's commitment to running automations on a hub at home is *the* differentiator versus Alexa/Google.

## Slide 24
PART 4 · APPLE HOME IN 2026
What Apple Home does well today
Hub built in
HomePod, HomePod mini, Apple TV 4K - already a hub AND a Thread border router.
Matter from day one
Apple was the first major platform to ship Matter at launch in 2022.
HomeKit Secure Video
Camera footage encrypted on-device, stored in iCloud, only your family can decrypt.
Adaptive Lighting
Bulbs shift warmth automatically through the day - native, no automation needed.
Activity history
See exactly when each device was triggered, by whom or what.
Multi-user, multi-home
Real family permissions across multiple addresses. Guest access for Airbnb.
SMMUG · The State of the Smart Home · May 11, 2026
Apple
21
Notes: Walk through each card briefly. Spend most time on HomeKit Secure Video - it's the one feature competitors can't match on privacy. Adaptive Lighting story: Apple just turned on a feature that worked across every HomeKit-certified bulb. No new hardware. That kind of orchestration is only possible because they control the platform. Multi-home and guest access make Apple Home shine for second homes or rentals.

## Slide 25
PART 4 · THE HONEST PART
The 2022-2023 Home architecture saga
Apple isn't perfect. Here's how I know.
Dec 2022
iOS 16.2 introduces the 'new Home architecture' - faster, more reliable, multi-admin ready.
Jan 2023
Users who upgrade start losing devices, getting stuck mid-migration. Apple pulls the upgrade prompt.
2023
Apple silently re-rolls the new architecture into iOS 16.4 / 16.5 with hardening fixes.
2024-26
Stable. But many longtime users still have PTSD from the rollout and watch every update closely.
Takeaway: Apple's strengths in privacy and design don't make them immune to software bugs. Stay one minor-version behind on smart-home gear for a week or two.
SMMUG · The State of the Smart Home · May 11, 2026
Apple
22
Notes: This is the honesty slide. The audience will appreciate that you're not selling them Apple. If anyone in the room has stories - and they will - this is a great place for 30 seconds of shared misery. Practical advice: in any smart-home product, hold off the .0 release of a new OS for a week or two.

## Slide 26
PART 4 · WHAT'S NEXT
Apple Intelligence meets your house
With Apple Intelligence shipping across iOS, iPadOS, and macOS - the smart home is the obvious next surface.
Natural automation
'When I leave for work, set the thermostat to 65 and lock the doors' - written, not coded.
Context-aware Siri
'Was the back door opened today?' answered from on-device activity history.
On-device processing
Routine intent stays on your Apple Silicon hub - cloud only when you say so.
Visual intelligence
Your camera footage gets indexed and queryable - 'show me when the package arrived.'
Reality check
Siri's overhaul has been the slowest-moving part of Apple Intelligence. Some 'home' features have slipped from 2025 to 2026 to 2027.
The platform's there. The voice layer is the bottleneck.
SMMUG · The State of the Smart Home · May 11, 2026
Apple
23
Notes: Be honest about Siri's slow Apple Intelligence rollout. Don't pretend. But the substrate - on-device LLMs, Apple Silicon in HomePod/Apple TV, end-to-end encryption - is exactly the right foundation for AI in the home. Bet: Apple is positioned best for *private* AI in the home. Amazon and Google are ahead on capability but behind on trust.

## Slide 27
PART FIVE
Hubs
Local vs. cloud. Open vs. walled. And what I actually run.
Notes: Transition: 'Now that we know the protocols, where do they all meet? In something we call a hub.'

## Slide 28
PART 5 · THE FUNDAMENTAL CHOICE
Local vs. cloud
It matters more than you think.
Local
Brain lives in your house
Works when internet is down
Faster response (no round trip to cloud)
Privacy: your data stays on your LAN
Survives company death
Steeper learning curve - usually.
Cloud
Brain lives in someone else's data center
Easiest setup, slick apps
Auto-updates, no maintenance
Cross-property and remote 'just works'
If the vendor goes dark, your devices brick
Your usage data feeds someone else's business model.
SMMUG · The State of the Smart Home · May 11, 2026
Hubs
24
Notes: Frame: 'This isn't a religious war. Most of us live in a blend. But you should know which side each gadget is on.' Apple Home is a HYBRID - hub processing is local, but remote access is iCloud relay. Cloud-only services are convenient until they aren't. We'll come back to dead ones in the graveyard section.

## Slide 29
PART 5 · THE HUB LANDSCAPE
Choosing a hub in 2026
Apple Home
HomePod / Apple TV
Local · Privacy-first · Matter-native
Amazon Alexa
Echo / eero
Cloud-first · Best voice · Ad-supported model
Google Home
Nest Hub / speakers
Cloud-first · Strong AI · Quieter on home now
SmartThings
Samsung Aeotec / Station
Hybrid · Open-ish · Wide protocol support
Hubitat Elevation
C-8 Pro (what I use)
Local · Power user · Rules engine
Homey Pro
Athom
Local · Beautiful UX · 7 radios in one box
Home Assistant
DIY (Raspberry Pi, NUC)
Local · Open source · Power-user paradise
HomeSeer
Z-Wave veteran
Local · Pro / prosumer · Dated UI
SMMUG · The State of the Smart Home · May 11, 2026
Hubs
25
Notes: Walk through each. The point isn't to recommend one - it's to show the range. Apple users in this room: the surprise is that Hubitat and Home Assistant are great *complements* to Apple Home, not replacements. Use a more capable hub to bring in Z-Wave and weird Zigbee gear, then expose them all to Apple Home as Matter/HomeKit devices.

## Slide 30
PART 5 · ONE USER'S PATH
My own hub journey
Not a recommendation - just a story of how the choices have evolved.
Late 2000s
HomeSeer
Best Windows-based Z-Wave hub of its era. Powerful, but Windows-only and very ugly.
Mid 2010s
Wink Hub 1 / 2
Beautiful app, mainstream-friendly. Z-Wave + Zigbee + Lutron. Then the cloud fell apart.
Late 2010s
(transition)
Wink started charging users for the service that used to be free. The trust was gone.
2020s
Hubitat Elevation C-8 Pro
Local-first, rule engine, fast. Survives internet outages. My current daily driver.
2020s
Homey Pro
Seven radios in one box (Z-Wave, Zigbee, Thread, Matter, BLE, IR, 433 MHz). Polished UX.
Optional
Home Assistant
On a Pi/NUC for the things no commercial hub will ever cover - the bottomless tinker box.
SMMUG · The State of the Smart Home · May 11, 2026
Hubs
26
Notes: This is the story slide - personal experience earns trust. Anchor on the moment Wink went bad: 'I'd recommended Wink to friends. When they started charging a monthly fee, I had to apologize for the recommendation.' Hubitat is the pragmatic recommendation for SMMUG members who want more than Apple Home alone can give them, without going all-the-way to Home Assistant.

## Slide 31
PART 6 · VOICE
Alexa vs. Google vs. Siri
Capability | Alexa | Google Assistant | Siri
Smart home control | Excellent | Excellent | Good, getting better
General knowledge Q&A | Strong (Alexa+ LLM, 2024+) | Strongest | Behind, leans on ChatGPT
Privacy posture | Cloud-first, opt-out on-device | Cloud-first | On-device by default
Multi-step routines | Best in class | Strong | Limited but improving
Local fallback | Some (with Echo Hub) | Minimal | Full local on hub
Subscription pressure | Alexa+ paid tier ($19.99/mo) | Free, ads in ecosystem | No subscription
Alexa+ in 2024 was a full rebuild on a Claude/Nova backbone. Siri's parallel rebuild has been... slower.
SMMUG · The State of the Smart Home · May 11, 2026
Voice + AI
27
Notes: Be even-handed. Each assistant is best at something different. Alexa+ is genuinely impressive at conversational smart home commands now ('Hey, set the mood for movie night, but leave one lamp on so the dog isn't anxious'). Apple's slow Siri rebuild is a real liability - admit it. For people in this room with privacy concerns, Siri is still the only major option that doesn't ship voice to the cloud by default.

## Slide 32
PART 6 · AI IN THE HOME
The agent era is starting
Smart home + LLMs is not 'better voice recognition.' It's a different kind of automation.
From rules to intent
Used to be: 'if door opens after 10pm, send notification.' Now: 'let me know if anything seems off tonight.'
Cross-device reasoning
An agent can combine the door sensor, camera, calendar, and weather to give you one helpful answer.
Natural setup
Setting up automations becomes a conversation, not a flowchart in an app.
The privacy question
Local LLMs (Apple Intelligence, Home Assistant Voice PE, Ollama on a NUC) vs. cloud LLMs (Alexa+, Gemini).
SMMUG · The State of the Smart Home · May 11, 2026
Voice + AI
28
Notes: Most useful framing: 'LLMs let us ask the house questions and describe goals - instead of programming it.' Local LLMs are real in 2026 - Home Assistant's Voice Preview Edition runs a 7B model on a NUC well enough for household use. Where this goes wrong: if a model hallucinates a 'helpful' action, it can be embarrassing. Manufacturers are appropriately cautious.

## Slide 33
PART SEVEN
Privacy, Security & Graveyards
The data, the breaches, and the stranded users.
Notes: Tone shift. The first two sections of this part are sobering. The third has a redemption arc. If you're running low on time, you can compress slides 33-36 into 2 slides.

## Slide 34
PART 7 · THE COST OF CONVENIENCE
What your smart home knows about you
Voice recordings
Cloud assistants ship every wake-word event to the cloud. Until 2023, humans reviewed samples.
Camera footage
Ring shared with police across 2,000+ jurisdictions before 2024 policy reversals.
Occupancy patterns
Sleep, wake, leave, return - your motion sensors create a behavior profile.
Network metadata
Even encrypted traffic reveals device types, vendors, and usage windows.
What you can do
Prefer local-control devices when possible
Use Matter / HomeKit for sensors and bulbs
Put smart-home gear on an IoT VLAN
Disable cloud history features you don't need
Review camera sharing settings annually
Choose vendors with end-to-end encryption
SMMUG · The State of the Smart Home · May 11, 2026
Privacy
29
Notes: Ring + police partnership: Ring Neighbors used to allow police to request video without a warrant. After major pushback they reversed this in 2024. Apple is the easiest privacy story to recommend to this audience because the defaults align with their preferences already. VLAN suggestion: most prosumer routers (eero, UniFi, ASUS) now support an IoT network with one click.

## Slide 35
PART 7 · THE GRAVEYARD
Products that took users with them
Revolv
R.I.P. 2016
Nest bought them, then bricked the hub via firmware kill. Industry-changing scandal.
Lowe's Iris
R.I.P. 2019
Closed with 30 days notice. Hubs and devices became paperweights overnight.
Wink
R.I.P. 2020
Suddenly imposed a $5/mo fee. Users walked. Status: barely operating.
Stringify
R.I.P. 2018
If-this-then-that competitor. Free, beloved, then deleted.
Insteon
R.I.P. 2022 / 2024
Servers went dark twice. Second time bricked the cloud-dependent fleet again.
Logitech Harmony
R.I.P. 2021
Logitech stopped selling Harmony hubs and remotes. Cloud is on borrowed time.
SMMUG · The State of the Smart Home · May 11, 2026
Graveyard
30
Notes: This is the cautionary tale. Tell the Revolv story in detail if you have time - Nest bought it, then deliberately disabled the hubs. Lesson seeded: cloud dependence is a single point of corporate failure. Lead-in to next slide: 'So how do we avoid putting our wallets and our walls into the next graveyard?'

## Slide 36
PART 7 · SURVIVAL RULES
How to pick gear that outlives its maker
Local control wins
If the device works without internet, the company can die and your home doesn't.
Open standards win
Matter, Thread, Z-Wave, Zigbee - if your gear speaks the language, someone else can take it over.
Beware single-vendor clouds
If your bulb only works via Acme Cloud, your bulb's life expectancy = Acme Cloud's.
Backup the firmware
On enthusiast gear, document the pairings - so you can rebuild fast on a new hub.
Diversify hubs
Don't put everything on one hub from one vendor. A second hub is cheap insurance.
Buy from open ecosystems
When in doubt, buy from companies whose business is hardware, not subscriptions.
SMMUG · The State of the Smart Home · May 11, 2026
Graveyard
31
Notes: The redemption arc - here's how to not be the next stranded user. If they remember nothing else from this part: 'Local control wins.'

## Slide 37
PART 8 · TWO WORLDS
DIY vs. pro install - and a middle path
DIY
Apple Home · SmartThings · Hubitat · Home Assistant
Cost: $0-$3,000 for a whole-home setup
Setup: you do it; install over a weekend
Support: forums, Reddit, you
Upgrade: as cheap as you want it to be
Middle path
Lutron Caseta · ecobee · Apple Home + a pro lighting installer
Cost: $5,000-$20,000
Setup: hire a pro for the wiring; you keep the app
Support: vendor + your installer
Upgrade: bring your own controller later
Pro install
Control4 · Crestron Home · Savant · Lutron HomeWorks
Cost: $25,000-$500,000+
Setup: integrator-driven, months not weekends
Support: dealer locked
Upgrade: requires the same dealer
SMMUG · The State of the Smart Home · May 11, 2026
DIY vs Pro
32
Notes: Most SMMUG members will live in column 1 (DIY) or column 2 (Middle Path) - especially Lutron Caseta + Apple Home is a fantastic combo. Column 3 (Crestron/Control4) is real but invisible to most consumers. Mention it for context. Pro install warning: dealer lock-in. If your dealer goes out of business, getting another integrator to take over a Crestron system is nontrivial.

## Slide 38
PART 8 · WHAT COULD HAVE BEEN
Why your house is harder than it should be
If the four big platforms had cooperated 10 years earlier, the smart home would already be solved.
Three voice assistants
Three different wake words. Three different cloud audit trails. Three different sets of skills/actions you have to maintain.
Bridge gymnastics
Until Matter, doing 'cross-platform' meant SmartThings → Home Bridge → Hue → IFTTT chains. Fragile every link.
Walled garden cameras
Ring footage stays in Ring. Nest footage stays in Nest. HomeKit Secure Video stays in iCloud. No standard.
Subscription drift
Each platform now wants $5-$20/mo. The 'one platform to rule them all' became 'one subscription per room.'
SMMUG · The State of the Smart Home · May 11, 2026
Industry
33
Notes: Vent moment - the audience will nod a lot here. Matter is the antidote, but it's a slow one. We're 4 years in and most users don't notice the difference yet. The real problem isn't technical - it's that 'lock-in' is each platform's growth strategy. Standards work against that.

## Slide 39
PART 8 · A BETTER FUTURE
What better looks like
One pairing experience
Scan a QR code; it lands on every hub in the house, not just one.
Vendor-agnostic camera storage
Encrypted video that any compatible app can render - so cameras can outlive the brand.
Portable automations
A 'when sunset, dim to 30%' rule that you can move between Apple, Google, and Hubitat.
Right-to-repair for IoT
When a company shuts a cloud, owners get the keys to the kingdom - documented, not improvised.
SMMUG · The State of the Smart Home · May 11, 2026
Industry
34
Notes: Optimistic note. Matter is a first step toward most of this list. Right-to-repair for IoT is a real legislative discussion in 2026 - watch your news for it. Encourage members to push their vendors: 'Why doesn't this camera support standard storage?' is a fair question to ask Ring or Nest in 2026.

## Slide 40
PART 8 · LOOKING FORWARD
Five predictions for 2026 - 2030
01
Matter wins quietly
By 2028, 'Works with Matter' will be the default badge - just like 'Bluetooth' became.
02
Local AI hubs become the norm
Apple, Google, and Amazon all ship LLMs that run at home, not in the data center.
03
Cameras become storage-portable
Pressure (and regulation) forces standard, encrypted formats - finally.
04
Energy management gets real
Smart panels, EVs, and home batteries finally talk to each other - and to the utility.
05
Voice loses the wake word
Ambient computing - the house just notices and asks, instead of you summoning.
SMMUG · The State of the Smart Home · May 11, 2026
Future
35
Notes: Be willing to be wrong - predictions invite debate, which is great for Q&A. Ambient computing - the cleanest framing of where this is all going. Worth a beat to let it sink in. Watch for SmartThings Energy, Apple's home-energy hints, and the rise of bidirectional EV charging.

## Slide 41
FOR SMMUG MEMBERS
A practical starter map
If I were setting up a smart home tomorrow in this room - here's what I'd buy.
Just exploring
1 HomePod mini + a Matter-over-Thread plug + a Matter bulb
Under $200, no commitments, all Apple-native.
Already in the ecosystem
Apple TV 4K as Thread hub + Lutron Caseta + Hue or Nanoleaf bulbs
Reliable, beautiful, all HomeKit-certified.
Want more control
Add Hubitat Elevation C-8 Pro or Homey Pro alongside Apple Home
Local rules engine, broader protocol support, exposes everything back to Apple.
Power user / tinkerer
Add Home Assistant on a Pi or NUC
Anything not supported elsewhere, plus full data sovereignty.
SMMUG · The State of the Smart Home · May 11, 2026
Recommendations
36
Notes: Personal! These are *my* recommendations, not a sales pitch. Customize on the fly: if someone asks about cameras, point to Logitech Circle View or Eve Outdoor Cam for HomeKit Secure Video. Mention you'll share a written version of this list in the Q&A.

## Slide 42
GOING DEEPER
Resources & rabbit holes
csa-iot.org
Matter spec, certified device list, working groups
threadgroup.org
The Thread spec and member directory
home-assistant.io
Open-source hub - even if you don't use it, the docs explain everything
hubitat.com
Local-first commercial hub - the C-8 Pro is the current sweet spot
homey.app
Homey Pro - polished Dutch alternative
developer.apple.com/homekit
Apple's official HomeKit / Matter materials
r/homeautomation
Reddit's smart-home community - chaotic but informed
The Verge / Stacey on IoT
Best mainstream and trade reporting respectively
SMMUG · The State of the Smart Home · May 11, 2026
Resources
37
Notes: Offer to share these as a written handout (PDF) after the talk. If asked: 'I'll send the slide deck and a PDF version to whoever signs the SMMUG email list.'

## Slide 43
Questions?
And: what's working - or not - in your house?
Thank you, SMMUG.
Jim Johnson · mahatmajim@gmail.com · May 11, 2026
Notes: Discussion seeds if Q&A is slow: · 'What's the one device in your house you wish you'd never bought?' · 'Who here has a Matter device they could share an experience with?' · 'Is anyone on Home Assistant - what do you wish you'd known on day one?' · 'How many of you have an Apple TV that's secretly already a Thread hub?' Close with: 'I'll be at the back if you want to talk specifics. Thanks for having me.'